## Slide 1
Industrial Edge AI Processor Selection
Heavy Deep Learning Inference & Real-Time Video Conferencing SoM / Carrier Board Evaluation — August 2026
August 2026 | Revision 1.0 | Confidential

## Slide 2
Executive Summary
PRIMARY RECOMMENDATION: Texas Instruments TDA4VM / AM68A
→ 8 TOPS AI accelerator, 4K video codec, ASIL-D safety, –40 °C to +105 °C junction
→ Dual-domain: Linux (A72) + FreeRTOS (R5F) for deterministic real-time control
→ Integrated ISP @ 480 MP/s, hardware H.264/H.265 encode/decode, TSN Ethernet
SECONDARY RECOMMENDATION: Rockchip RK3588
→ 6 TOPS NPU, 8K encode/decode, dual 2.5 GbE, industrial modules –40 °C to +85 °C
→ Best price/performance for multi-channel AI video gateways
TERTIARY: NXP i.MX 95 — 10–15 year supply, TSN, 2 TOPS NPU, mature Yocto/FreeRTOS BSP
CAVEAT OPTIONS (Temp limited): Qualcomm QCS6490 (12 TOPS, –30 °C min) | NVIDIA Jetson Orin NX (100 TOPS, –25 °C min)
All platforms evaluated against: –40 °C min temp, hardware AI ≥2 TOPS, H.264/H.265 codec, mature C/C++ toolchain, RTOS/Linux support.

## Slide 3
Selection Criteria & Requirements
TEMPERATURE: Industrial grade –40 °C to +85 °C ambient (junction –40 °C to +105 °C preferred)
AI COMPUTE: Dedicated NPU/DSP/GPU ≥ 2 TOPS INT8 for on-device deep learning inference
VIDEO CONFERENCING: Hardware-accelerated H.264/H.265 simultaneous encode + decode
VISION: Integrated ISP with HDR, multi-camera MIPI-CSI support, ≥ 375 MP/s throughput
TOOLCHAIN: Mature C/C++ SDK, Yocto/Buildroot BSP, FreeRTOS/Zephyr bare-metal support
FRAMEWORKS: TensorFlow Lite, ONNX Runtime, or vendor-optimised edge-AI runtime
CONNECTIVITY: Gigabit Ethernet (TSN preferred), USB 3.x, PCIe for expansion
SAFETY: ECC memory, secure boot, functional-safety certification (ASIL / SIL) where applicable
LONGEVITY: 10–15 year supply commitment from vendor

## Slide 4
Platform Deep Dives

## Slide 5
01 | Texas Instruments TDA4VM / AM68A — PRIMARY RECOMMENDATION
KEY SPECIFICATIONS
• CPU: 2× Cortex-A72 @ 2.0 GHz + 6× Cortex-R5F @ 1.0 GHz
• AI Accelerator: MMA 8 TOPS (INT8) + C7x DSP 80 GFLOPS
• GPU: PowerVR Rogue 8XE GE8430 @ 750 MHz (96 GFLOPS)
• RAM: Up to 8 GB LPDDR4-4266 (inline ECC)
• Video Codec: Decode: 1× 4K@60 / 4× 1080p60 | Encode: 1× 1080p60 / 3× 1080p30
• ISP: 480 MP/s, HDR, dewarp, lens shading
• Camera: 2× MIPI CSI-2 4L RX + 1× CSI-2 4L TX
• Ethernet: 8-port GbE switch (2.5 Gb SGMII), TSN
• Safety: Targeted ASIL-D / SIL-3, AEC-Q100
• OS: Linux (Yocto), QNX, FreeRTOS, SafeRTOS
• TDP: 5–10 W (passive cooling viable)
• Supply: Guaranteed to 2036+
AI & IMAGE PROCESSING CAPABILITIES
• Heavy DL inference: YOLOv5s @ ~45 fps, ResNet-50 @ ~35 fps (INT8)
• Real-time conferencing: Hardware H.264 encode offloads CPU completely
• GStreamer plugins provided by TI for accelerated AV pipeline
• 6× R5F cores enable deterministic audio/control loops parallel to Linux AI pipeline
• Lockstep R5F pair for safety-critical monitoring without hypervisor
• Dual-OS: Linux handles vision/AI while FreeRTOS manages real-time I/O
COMMERCIAL & MECHANICAL DATA
• SoM Available: Yes — PHYTEC (57×54 mm), Congatec SMARC (82×50 mm), Bit Mapper (80×80 mm)
• Carrier Board Available: Yes — Evaluation kits from PHYTEC, Congatec, Bit Mapper; custom carriers available
• SoM Dimensions: 57 × 54 mm (PHYTEC) | 82 × 50 mm (SMARC) | 80 × 80 mm (Bit Mapper)
• Carrier Board Lead Time: Eval kit: 2–4 weeks | Custom carrier design: 10–14 weeks | Volume production: 16–20 weeks
• Temp Rating: –40 °C to +105 °C (Junction) — EXCEEDS REQUIREMENT

## Slide 6
02 | Rockchip RK3588 — SECONDARY RECOMMENDATION
KEY SPECIFICATIONS
• CPU: 4× Cortex-A76 @ 2.4 GHz + 4× Cortex-A55 @ 1.8 GHz
• AI Accelerator: Triple-core NPU 6 TOPS (INT8/INT4/FP16 hybrid)
• GPU: Arm Mali-G610 MP4 (OpenCL 2.2, Vulkan 1.1)
• RAM: Up to 32 GB LPDDR4x/LPDDR5
• Video Codec: Decode: 8K@60 H.265, 8K@30 H.264 | Encode: 8K@30 H.265/H.264
• ISP: 48 MP ISP 3.0, HDR, 3D NR, dehaze, fisheye correction
• Camera: 2× 4-lane MIPI CSI (up to 4 concurrent cameras)
• Ethernet: Dual 2.5 GbE + Wi-Fi 6 / BT 5.0
• Safety: Industrial module validation (no formal ASIL)
• OS: Linux (Yocto/Buildroot), Android 12/13
• TDP: 8–12 W (large heatsink for sustained 8K)
• Supply: 2033+ (industrial module vendors)
AI & IMAGE PROCESSING CAPABILITIES
• Highest codec bandwidth in class: simultaneous 8K encode + 8K decode
• Multi-channel AI gateway: run per-camera analytics on 4+ streams concurrently
• RKNN Toolkit 2.0 supports ONNX, TFLite, PyTorch model conversion
• 2D Pixel Processing Accelerator for image pre-processing before NPU inference
• Ideal for smart NVR, AI security gateway, video doorbell arrays
• Industrial modules from Forlinx, Qiyang, Geniatech validated –40 °C to +85 °C
COMMERCIAL & MECHANICAL DATA
• SoM Available: Yes — Forlinx FET3588-C (68×50 mm), Qiyang, Geniatech, many vendors
• Carrier Board Available: Yes — Forlinx carrier (190×130 mm), Qiyang carrier, custom designs available
• SoM Dimensions: 68 × 50 mm (Forlinx SoM) | 82 × 50 mm (SMARC variants)
• Carrier Board Lead Time: Eval kit: 1–2 weeks | Custom carrier design: 8–12 weeks | Volume: 12–16 weeks
• Temp Rating: –40 °C to +85 °C (Industrial modules) — MEETS REQUIREMENT

## Slide 7
03 | NXP i.MX 95 — TERTIARY RECOMMENDATION
KEY SPECIFICATIONS
• CPU: 6× Cortex-A55 @ 2.0 GHz + M7 @ 800 MHz + M33 @ 333 MHz
• AI Accelerator: eIQ Neutron NPU 2 TOPS (INT8)
• GPU: Arm Mali-G310 (Vulkan 1.3, OpenGL ES 3.2)
• RAM: Up to 16 GB LPDDR5 (inline ECC)
• Video Codec: 4K@60 H.265/H.264 encode/decode
• ISP: Dual ISP, multi-camera input support
• Camera: MIPI CSI-2 interfaces
• Ethernet: Dual GbE (1× TSN), 10 GbE option
• Safety: EdgeLock secure enclave, inline DRAM ECC, functional-safety support
• OS: Linux (Yocto/RT Edge), FreeRTOS, Zephyr
• TDP: 5–8 W
• Supply: Guaranteed to 2038+ (NXP longevity programme)
AI & IMAGE PROCESSING CAPABILITIES
• Best-in-class supply longevity: 10–15 year commitment from NXP
• TSN-enabled Ethernet for deterministic AVB and Industry 4.0 control traffic
• eIQ Toolkit: TensorFlow Lite, ONNX Runtime, PyTorch, DeepViewRT
• Cortex-M7 + M33 provide hard real-time control alongside Linux AI stack
• Sufficient for medium-complexity models: YOLOv5s, MobileNet-SSD, gesture recognition
• Preempt-RT Linux patches available for low-latency conferencing pipelines
COMMERCIAL & MECHANICAL DATA
• SoM Available: Yes — Variscite DART-MX95 (55×30 mm), CompuLab UCM-iMX95 (28×40 mm)
• Carrier Board Available: Yes — DART-MX95 eval kit, UCM eval kit ($645), custom carrier design services
• SoM Dimensions: 55 × 30 mm (DART) | 28 × 40 mm (UCM)
• Carrier Board Lead Time: Eval kit: 2–4 weeks | Custom carrier design: 8–12 weeks | Volume: 14–18 weeks
• Temp Rating: –40 °C to +85 °C (Industrial SKUs) — MEETS REQUIREMENT

## Slide 8
04 | NXP i.MX 8M Plus — PROVEN INDUSTRIAL OPTION
KEY SPECIFICATIONS
• CPU: 4× Cortex-A53 @ 1.8 GHz + 1× Cortex-M7 @ 800 MHz
• AI Accelerator: Dedicated NPU 2.3 TOPS (INT8)
• GPU: GC7000UL (16 GFLOPS, OpenGL ES 3.1, Vulkan)
• RAM: Up to 8 GB LPDDR4 (inline ECC)
• Video Codec: 1080p60 H.265/H.264/VP9 encode/decode
• ISP: Dual ISP, 375 MP/s, 12 MP, HDR, dewarp
• Camera: 2× 4-lane MIPI CSI-2
• Ethernet: Dual GbE (1× TSN), 2× CAN-FD
• Safety: IEC 61508 / ISO 26262 certified, DRAM inline ECC
• OS: Linux (Yocto), Android, FreeRTOS, QNX
• TDP: 3–5 W (lowest in class)
• Supply: Guaranteed to 2036+
AI & IMAGE PROCESSING CAPABILITIES
• Proven, shipping platform with extensive safety certification
• Lowest TDP and BOM cost — ideal for cost-sensitive smart cameras
• Dual ISP enables simultaneous visible + IR camera processing
• 1080p60 codec adequate for standard-definition conferencing and IP cameras
• eIQ + CMSIS-NN for TFLite and ONNX model deployment
• Mature ecosystem: Variscite, CompuLab, Emcraft, Geniatech modules available
COMMERCIAL & MECHANICAL DATA
• SoM Available: Yes — Variscite (67.8×33 mm), CompuLab (28×38 mm), Emcraft (58.4×58.4 mm), Geniatech SMARC (82×50 mm)
• Carrier Board Available: Yes — Dahlia, SMARC carrier boards, eval kits from all major vendors
• SoM Dimensions: 67.8 × 33 mm (VAR-SOM) | 28 × 38 mm (UCM) | 58.4 × 58.4 mm (Emcraft) | 82 × 50 mm (SMARC)
• Carrier Board Lead Time: Eval kit: 1–3 weeks | Custom carrier design: 6–10 weeks | Volume: 10–14 weeks
• Temp Rating: –40 °C to +105 °C (Junction) — EXCEEDS REQUIREMENT

## Slide 9
05 | Qualcomm QCS6490 — HIGH PERF. (TEMP. CAVEAT)
KEY SPECIFICATIONS
• CPU: 8× Kryo 670 (1× 2.7 + 3× 2.4 + 4× 1.9 GHz)
• AI Accelerator: Hexagon 770 DSP 12 TOPS (dense INT8)
• GPU: Adreno 643 (812 MHz, OpenGL ES 3.2, Vulkan)
• RAM: Up to 16 GB LPDDR5
• Video Codec: Decode: 1× 4K@80 / 4× 1080p60 | Encode: 1× 4K@30 / 4× 1080p30
• ISP: Spectra 570L triple ISP, 5× cameras, 64 MP ZSL
• Camera: 5× 4-lane MIPI CSI (D-PHY / C-PHY)
• Ethernet: Via companion chip (QPS615) — dual GbE
• Safety: —
• OS: Android 13, Linux (Yocto 5.0), Ubuntu, Win11 IoT
• TDP: 6–9 W
• Supply: 2036+
AI & IMAGE PROCESSING CAPABILITIES
• Highest AI throughput in mid-range class: 12 TOPS for complex models
• Triple ISP supports 5 concurrent cameras — ideal for surround-view systems
• Qualcomm SNPE + ONNX Runtime for optimised model deployment
• Adreno GPU supports advanced UI rendering alongside AI inference
• Best for premium robotics, high-end HMI, and multi-camera AI gateways
• ⚠️ TEMPERATURE LIMITATION: –30 °C minimum — NOT suitable for –40 °C cold-start
COMMERCIAL & MECHANICAL DATA
• SoM Available: Yes — Aikri (65×40 mm), MitySOM (45×45 mm), Geniatech OSM (45×45 mm), SECO SMARC (82×50 mm), Lantronix (47×35 mm)
• Carrier Board Available: Yes — Tessolve carrier, evaluation kits from Arrow/eInfochips, Lantronix
• SoM Dimensions: 45 × 45 mm (MitySOM/OSM) | 65 × 40 mm (Aikri) | 82 × 50 mm (SMARC) | 47 × 35 mm (Lantronix)
• Carrier Board Lead Time: Eval kit: 3–5 weeks | Custom carrier design: 10–14 weeks | Volume: 14–20 weeks
• Temp Rating: –30 °C to +105 °C (Tj) — DOES NOT MEET –40 °C REQUIREMENT

## Slide 10
06 | NVIDIA Jetson Orin NX — HIGH PERF. (TEMP. CAVEAT)
KEY SPECIFICATIONS
• CPU: 8× Cortex-A78AE @ 2.0 GHz
• AI Accelerator: Ampere GPU + Tensor Cores 100 TOPS (INT8)
• GPU: Ampere (shared with AI, CUDA support)
• RAM: Up to 16 GB LPDDR5
• Video Codec: Decode: 1× 4K@60 / 8× 1080p30 | Encode: 1× 4K@60 / 6× 1080p60
• ISP: Up to 7 cameras via virtual channels
• Camera: Up to 16-lane MIPI CSI (4× 4L + 2× 2L)
• Ethernet: 1× GbE (via carrier board expansion)
• Safety: —
• OS: Linux (JetPack / Ubuntu)
• TDP: 10–25 W (active cooling required)
• Supply: 2033+
AI & IMAGE PROCESSING CAPABILITIES
• Unmatched AI performance: 100 TOPS enables large-model inference at the edge
• TensorRT + CUDA ecosystem for advanced AI research and deployment
• Excellent for autonomous machines, advanced robotics, and AI R&D platforms
• 4K@60 encode/decode with broad codec support (H.265, AV1, VP9)
• Massive ecosystem: Connect Tech, Auvidea, AVerMedia, Seeed carrier boards
• ⚠️ TEMPERATURE LIMITATION: –25 °C minimum — NOT suitable for –40 °C cold-start
• ⚠️ No bare-metal / RTOS path — Linux-only platform
COMMERCIAL & MECHANICAL DATA
• SoM Available: Yes — NVIDIA module 100×79×21 mm (260-pin SODIMM edge connector)
• Carrier Board Available: Yes — NVIDIA dev kit, Connect Tech, Auvidea, AVerMedia, Seeed, Antmicro (50+ vendors)
• SoM Dimensions: 100 × 79 × 21 mm (NVIDIA module)
• Carrier Board Lead Time: Eval kit: 1–2 weeks | Custom carrier design: 8–12 weeks | Volume: 12–16 weeks
• Temp Rating: –25 °C to +85 °C (Extended) — DOES NOT MEET –40 °C REQUIREMENT

## Slide 11
Comparative Matrix — SoM / Carrier / Dimensions / Lead Time
Platform | SoM Available | Carrier Available | SoM Dimensions | Carrier Lead Time | Temp Range | AI TOPS | Video Codec
TI TDA4VM/ AM68A | ✓ Yes (3 vendors) | ✓ Yes | 57×54 / 82×50 / 80×80 mm | Eval: 2–4 wks Custom: 10–14 wks | –40 to +105 °C | 8 | 4K60 dec 1080p60 enc
Rockchip RK3588 | ✓ Yes (5+ vendors) | ✓ Yes | 68×50 / 82×50 mm | Eval: 1–2 wks Custom: 8–12 wks | –40 to +85 °C | 6 | 8K60 dec 8K30 enc
NXP i.MX 95 | ✓ Yes (2 vendors) | ✓ Yes | 55×30 / 28×40 mm | Eval: 2–4 wks Custom: 8–12 wks | –40 to +85 °C | 2 | 4K60 enc/dec
NXP i.MX 8M Plus | ✓ Yes (4+ vendors) | ✓ Yes | 67.8×33 / 28×38 / 58.4×58.4 / 82×50 | Eval: 1–3 wks Custom: 6–10 wks | –40 to +105 °C | 2.3 | 1080p60 enc/dec
Qualcomm QCS6490 | ✓ Yes (5 vendors) | ✓ Yes | 45×45 / 65×40 / 82×50 / 47×35 mm | Eval: 3–5 wks Custom: 10–14 wks | –30 to +105 °C ⚠ | 12 | 4K80 dec 4K30 enc
NVIDIA Jetson Orin NX | ✓ Yes (NVIDIA) | ✓ Yes (50+ vendors) | 100×79×21 mm | Eval: 1–2 wks Custom: 8–12 wks | –25 to +85 °C ⚠ | 100 | 4K60 enc/dec

## Slide 12
AI Inference Performance Benchmarks (INT8, Representative)
Model | TI TDA4VM (8 TOPS) | RK3588 (6 TOPS) | i.MX 95 (2 TOPS) | i.MX 8M Plus (2.3 TOPS) | QCS6490 (12 TOPS) | Jetson Orin NX (100 TOPS)
ResNet-50 | ~35 fps | ~28 fps | ~10 fps | ~11 fps | ~55 fps | ~450 fps
YOLOv5s @ 1080p | ~45 fps | ~38 fps | ~12 fps | ~14 fps | ~70 fps | ~600 fps
YOLOv8m @ 1080p | ~18 fps | ~15 fps | ~5 fps | ~6 fps | ~28 fps | ~240 fps
MobileNet-SSD @ 1080p | ~120 fps | ~100 fps | ~35 fps | ~40 fps | ~180 fps | ~1500 fps
Pose Est. (MoveNet) | ~55 fps | ~45 fps | ~15 fps | ~18 fps | ~85 fps | ~700 fps
Note: Benchmarks are indicative. Actual performance depends on model quantisation, memory bandwidth, compiler optimisations, and thermal conditions.

## Slide 13
Real-Time Video Conferencing Subsystem Analysis
CRITICAL PATH LATENCY BUDGET (30 fps conferencing, ITU-T G.114 <150 ms one-way):
→ ISP processing: <5 ms per frame | Video encode: <10 ms | Network + jitter: <50 ms | Decode + render: <10 ms
PLATFORM SUITABILITY FOR CONFERENCING:
• TI TDA4VM — 1× 1080p60 encode + 4× 1080p60 decode simultaneously. GStreamer plugins from TI abstract HW codec.
→ 6× R5F cores run deterministic audio path (MCASP) in parallel with Linux AV pipeline. TSN Ethernet for AVB.
• Rockchip RK3588 — 8K encode + 8K decode. Highest bandwidth. Best for multi-participant gateway (4+ streams).
→ No TSN support. Linux-only audio path.
• NXP i.MX 95 — 4K60 encode/decode. TSN GbE. M7/M33 RTOS cores for deterministic audio. 2-TOPS NPU for light AI overlay.
• NXP i.MX 8M Plus — 1080p60 encode/decode. Adequate for SD conferencing. TSN GbE. Lowest power.
• Qualcomm QCS6490 — 4K30 encode + 4K80 decode. Triple ISP. Best for premium multi-camera conferencing bars.
→ ⚠️ –30 °C limit. No TSN. Companion chip required for dual GbE.
• NVIDIA Jetson Orin NX — 4K60 encode/decode. 100 TOPS enables AI background blur / noise suppression on-device.
→ ⚠️ –25 °C limit. Active cooling required. No RTOS/bare-metal path.

## Slide 14
Recommendations by Application Profile
SAFETY-CRITICAL INDUSTRIAL VISION + CONFERENCING → TEXAS INSTRUMENTS TDA4VM / AM68A
→ Only platform with ASIL-D / SIL-3 targeting, lockstep R5F cores, full ECC, and –40 °C cold-start.
→ Dual-domain architecture guarantees deterministic safety loops alongside AV pipelines.
MULTI-CHANNEL AI VIDEO GATEWAY (4+ CAMERAS) → ROCKCHIP RK3588
→ Unmatched codec bandwidth (8K enc/dec) enables simultaneous transcoding of multiple conference streams.
→ 6-TOPS NPU supports per-channel AI analytics concurrently. Best price/performance.
LONG-LIFE INDUSTRIAL HMI WITH LIGHT AI → NXP i.MX 95
→ 10–15 year supply guarantee and mature Yocto/FreeRTOS ecosystem minimise re-certification risk.
→ TSN-enabled Ethernet supports Industry 4.0 deterministic AV and control traffic.
COST-SENSITIVE SMART CAMERA / DOOR PHONE → NXP i.MX 8M Plus
→ Lowest TDP (3–5 W) and BOM cost. Dual ISP and 1080p60 codec ideal for 2–3 MP cameras.
→ Proven shipping volume with IEC 61508 / ISO 26262 certification.
HIGH-PERFORMANCE RESEARCH / NON-CRITICAL ROBOTICS → Qualcomm QCS6490 OR NVIDIA Jetson Orin NX
→ QCS6490: 12 TOPS, 4K conferencing, –30 °C min (acceptable for climate-controlled environments).
→ Jetson Orin NX: 100 TOPS, CUDA ecosystem, –25 °C min (best for AI R&D and autonomous machines).

## Slide 15
Procurement, Supply Chain & Carrier Board Development
SoM vs. CHIP-LEVEL DESIGN TRADE-OFF:
→ SoM approach reduces time-to-market by 6–9 months. Carrier board design is simpler (2–6 layers) vs. 10–14 layer SoM.
→ SoM vendors provide reference schematics, BOM, PCB layout, and free design review (CompuLab, Variscite, PHYTEC).
→ Custom carrier boards typically require: schematic capture (2–3 wks) → PCB layout (2–4 wks) → fabrication (1–2 wks) → bring-up (2–3 wks).
LEAD TIME SUMMARY:
→ Evaluation kits: 1–5 weeks (stock dependent)
→ Custom carrier board design + prototype: 6–14 weeks (depends on layer count and vendor support)
→ Volume production ramp: 10–20 weeks after prototype validation
→ Component sourcing (LPDDR5, PMIC, connectors) is the critical path — allocate 8–12 weeks for long-lead parts
SUPPLY LONGEVITY & RISK:
→ LOW RISK: NXP (2038+), Texas Instruments (2036+), Qualcomm (2036+)
→ MEDIUM RISK: Rockchip (2033+), NVIDIA (2033+)
→ For safety-critical / medical / automotive: prioritise NXP and TI with formal PCN (Product Change Notification) programmes.
INDUSTRIAL MODULE VENDORS (Verified –40 °C to +85 °C):
→ TI: PHYTEC, Congatec, Bit Mapper | Rockchip: Forlinx, Qiyang, Geniatech | NXP: Variscite, CompuLab, Emcraft
→ Qualcomm: Aikri/Arrow, MitySOM/Critical Link, Geniatech, SECO, Lantronix | NVIDIA: NVIDIA, Connect Tech, Auvidea, AVerMedia

## Slide 16
FINAL RANKED SHORTLIST
1. TEXAS INSTRUMENTS TDA4VM / AM68A
Best overall balance of AI compute, AV codec, functional safety, and extreme-temperature operation.
2. ROCKCHIP RK3588
Best codec performance and cost efficiency for multi-channel AI video gateways.
3. NXP i.MX 95
Best long-term industrial support, TSN networking, and supply longevity.
4. NXP i.MX 8M Plus
Best for cost-sensitive, safety-certified 1080p vision and conferencing applications.
5. Qualcomm QCS6490 / NVIDIA Jetson Orin NX
Reserved for high-performance use cases where –30 °C / –25 °C cold-start is acceptable.
Document: Industrial Edge AI Processor Selection | August 2026 | Revision 1.0