## Slide 1
Industrial-Grade Edge AI
Processor Selection
Technical selection for heavy deep-learning inference and real-time video conferencing in industrial environments
Technical Evaluation — Internal Use
13 August 2026 | Revision 1.0
AI
8 TOPS
VIDEO
4K / 1080p
TEMP
−40…+85°C

## Slide 2
Executive Summary
Selection outcome and decision context
01
TDA4VM / AM68A
Primary platform
RK3588
Secondary
8 TOPS INT8
AI accelerator
−40…+105°C
Industrial junction
2036+
Supply
Why TDA4VM / AM68A leads
Converges heavy edge AI, hardware video, integrated vision processing and deterministic real-time control. The report identifies it as the strongest overall balance for harsh industrial deployments.
When RK3588 becomes the better fit
Choose when 8K multimedia bandwidth, multi-channel video analytics and cost efficiency are the dominant drivers, with industrial-grade module qualification available.
Decision principle: industrial temperature + deterministic real-time + AI + hardware AV must be evaluated together.
Technical Evaluation • Internal Use • Revision 1.0
2

## Slide 3
System Requirements
Mandatory and high-priority requirements from the technical report
02
ID | Requirement | Priority
FR-01 | Ambient −40°C to +85°C; minimum −40°C to +70°C | Mandatory
FR-02 | On-device heavy DL inference | Mandatory
FR-03 | Real-time bidirectional video conferencing | Mandatory
FR-04 | Hardware H.264 / H.265 encode & decode | Mandatory
FR-05 | Integrated ISP, HDR, multi-camera | High
FR-06 | C/C++ + RTOS path alongside Linux | High
FR-07 | TFLite / ONNX Runtime or equivalent | Mandatory
FR-08 | Gigabit Ethernet / high-speed wireless | High
FR-09 | Functional safety + 10–15 year supply | Medium
Real-time target
Dedicated RTOS core; <1 ms jitter
Thermal target
Passive cooling preferred
Reliability
ECC + secure boot + hardware crypto
Technical Evaluation • Internal Use • Revision 1.0
3

## Slide 4
Evaluation Methodology
Weighted decision framework used in the report
03
AI Compute Density
25%
INT8 TOPS, utilisation, framework support
Video Conferencing
25%
Codec concurrency, ISP, AV pipeline
Industrial Ruggedness
20%
Temperature, ECC, safety, MTBF
Software Maturity
15%
BSP, Yocto, GStreamer/V4L2, RTOS
I/O & Integration
15%
Camera, Ethernet, USB, PCIe, modules
Screening rule: only platforms with publicly confirmed industrial-temperature silicon or industrial-grade SoM variants were considered.
Technical Evaluation • Internal Use • Revision 1.0
4

## Slide 5
Platform Landscape
Six evaluated platform families
04
TI TDA4VM / AM68A
8 TOPS INT8 −40…+85°C Primary
Rockchip RK3588
6 TOPS INT8 −40…+85°C* Secondary
NXP i.MX 95
2 TOPS INT8 −40…+85°C Tertiary
NXP i.MX 8M Plus
2.3 TOPS INT8 −40…+85°C Proven
Qualcomm QCS6490
12 TOPS INT8 −30…+105°C Tj Caveat
NVIDIA Jetson Orin NX
100 TOPS INT8 −25…+85°C Caveat
* Industrial RK3588 module variants are reported as −40°C to +85°C ambient; consumer variants are not equivalent.
Technical Evaluation • Internal Use • Revision 1.0
5

## Slide 6
Primary Recommendation — TI TDA4VM / AM68A
Converged architecture for AI, AV and deterministic control
05
8 TOPS INT8
AI
C7x • 80 GFLOPS
DSP
480 MP/s
ISP
6× Cortex-R5F
RT cores
ASIL-D / SIL-3 target
Safety
Compute & real-time
Dual Cortex-A72 application CPUs plus six Cortex-R5F MCUs. Two R5F cores are in an isolated lockstep safety domain. C7x DSP + Deep-Learning MMA provides the AI acceleration path.
Vision & conferencing
480 MP/s ISP with HDR/dewarp. Hardware decode supports 4K and multiple 1080p streams. CSI-2 camera connectivity and hardware encode/decode enable a low-CPU AV pipeline.
Industrial fit
−40°C to +105°C junction; ECC; Linux + FreeRTOS/SafeRTOS; ONNX/TFLite via TIDL; GStreamer/V4L2.
Technical Evaluation • Internal Use • Revision 1.0
6

## Slide 7
Secondary Recommendation — Rockchip RK3588
Best multimedia bandwidth and multi-channel gateway profile
06
6 TOPS INT8
NPU
8K @ 60
Decode
8K @ 30
Encode
Up to 32 GB
Memory
Dual 2.5 GbE
Network
Why it excels
Highest hardware codec bandwidth in the evaluation. Supports 8K encode/decode, up to four concurrent camera inputs, strong ISP features and a broad industrial module ecosystem.
AI + software
Triple-core NPU supports INT4/INT8/INT16/FP16 hybrid operations. RKNN Toolkit 2.0 supports ONNX/TFLite conversion and INT8 quantisation; Linux, Buildroot and Yocto are available.
Trade-off
Excellent performance-per-dollar, but safety-critical deployments may require additional environmental qualification and ecosystem due diligence.
Technical Evaluation • Internal Use • Revision 1.0
7

## Slide 8
NXP Options
Balanced industrial lifecycle and safety-oriented alternatives
07
i.MX 95 — Long-life industrial HMI
• 2 TOPS INT8 Neutron NPU • 6× Cortex-A55 + M7 + M33 • 4Kp60 H.264/H.265/VP9 encode/decode • Dual ISP; multi-camera • Dual GbE, one with TSN • Inline DRAM ECC • −40°C to +85°C industrial SKUs • Supply stated through 2038+ • Best for Industry 4.0, robotics and deterministic HMI
i.MX 8M Plus — Cost-sensitive smart camera
• 2.3 TOPS NPU • 4× Cortex-A53 + M7 • 1080p60 H.264/H.265 encode/decode • Dual ISP, 375 MP/s • Dual GbE, TSN on one interface • Inline ECC • −40°C to +105°C junction • IEC 61508 / ISO 26262 • Best for smart cameras and 1080p conferencing
Technical Evaluation • Internal Use • Revision 1.0
8

## Slide 9
High-Performance Platforms with Temperature Caveats
Powerful AI, but outside the strict −40°C cold-start requirement
08
Qualcomm QCS6490
12 dense TOPS • 4K-class video • triple ISP • up to five concurrent cameras Temperature: −30°C to +105°C junction Best fit: high-end robotics, premium conferencing bars and AI gateways where −30°C is acceptable.
NVIDIA Jetson Orin NX
100 TOPS INT8 • Ampere GPU/Tensor Cores • 4K video • up to seven cameras Temperature: −25°C to +85°C module range Best fit: high-performance autonomous machines and AI research platforms where extreme cold-start is not a factor.
Recommendation: use only when environmental constraints are relaxed or active thermal management is feasible.
Technical Evaluation • Internal Use • Revision 1.0
9

## Slide 10
Comparative Technical Matrix
Decision-driving specifications from the report
09
Technical Evaluation • Internal Use • Revision 1.0
10
Comparative Technical Matrix
Complete engineering comparison including compute, video, memory, reliability, power, thermal behaviour and software platform
Parameter | TI TDA4VM / AM68A | Rockchip RK3588 | NXP i.MX 95 | NXP i.MX 8M Plus | Qualcomm QCS6490 | NVIDIA Orin NX
Temp | −40…+85°C | −40…+85°C* | −40…+85°C | −40…+85°C | −30…+105°C Tj | −25…+85°C
AI TOPS | 8 | 6 | 2 | 2.3 | 12 | 100
Decode | 4K / multi-1080p | 8K60 | 4K60 | 1080p60 | 4K80 | 4K60
Encode | 1080p60 / 3×1080p30 | 8K30 | 4K60 | 1080p60 | 4K30 / 4×1080p30 | 4K60
ISP | 480 MP/s | 48 MP | Dual | 375 MP/s | Spectra 570L | —
RAM | 8 GB | 32 GB | 16 GB | 8 GB | 16 GB | 16 GB
ECC | Yes | No | Yes | Yes | No | No
TSN | 2.5Gb SGMII | No | Yes | Yes | No | No
TDP Typical | 5 W | 8 W | 5 W | 3 W | 6 W | 10 W
Supply | 2036+ | 2033+ | 2038+ | 2036+ | 2036+ | 2033+
Power Consumption | Typical 5 W Peak 10 W | Typical 8 W Peak 12 W | Typical 5 W Peak 8 W | Typical 3 W Peak 5 W | Typical 6 W Peak 9 W | Typical 10 W Peak 25 W
Thermal / Cooling | −40…+85°C ambient; +105°C junction Passive: Excellent | −40…+85°C* Passive: Good | −40…+85°C Passive: Excellent | −40…+85°C ambient; +105°C junction Passive: Excellent | −30…+105°C junction Passive: Moderate | −25…+85°C module Passive: Poor
OS / Linux BSP | Yocto / Debian | Buildroot / Yocto / Debian | Yocto | Yocto / Android | Qualcomm Linux / Android | JetPack / Ubuntu
Source: Industrial-Grade Edge AI Processor Selection Presentation, Rev. 1.0. Power/Thermal from Thermal & Reliability; OS/BSP from Software Ecosystem & Development.

## Slide 11
Real-Time Video Conferencing Architecture
Deterministic capture-to-display path
10
CAMERA
MIPI-CSI
ISP
HDR / WDR
ENCODE
H.264 / H.265
NETWORK
RTP / RTSP / WebRTC
DECODE
Hardware VPU
DISPLAY
Render
Peer stream: NETWORK ← DECODE ← DISPLAY
< 5 ms
ISP budget
< 10 ms
Encode budget
< 50 ms
Network + jitter
< 10 ms
Decode + render
Target one-way interactive video latency: < 150 ms
Technical Evaluation • Internal Use • Revision 1.0
11

## Slide 12
Representative AI Inference Benchmarks
Indicative INT8 performance reported in the source document
11
Model | TDA4VM | RK3588 | i.MX 95 | i.MX 8M+ | QCS6490 | Orin NX
ResNet-50 | ~35 fps | ~28 | ~10 | ~11 | ~55 | ~450
YOLOv5s | ~45 fps | ~38 | ~12 | ~14 | ~70 | ~600
YOLOv8m | ~18 fps | ~15 | ~5 | ~6 | ~28 | ~240
MobileNet-SSD | ~120 fps | ~100 | ~35 | ~40 | ~180 | ~1500
MoveNet | ~55 fps | ~45 | ~15 | ~18 | ~85 | ~700
Interpretation
TDA4VM offers a strong industrial balance; Orin NX/QCS6490 provide much higher peak AI throughput but fail the strict −40°C requirement.
Important qualification
The report states benchmarks are indicative and depend on quantisation, memory bandwidth and compiler optimisation.
Technical Evaluation • Internal Use • Revision 1.0
12

## Slide 13
Thermal & Reliability
Passive-cooling feasibility and industrial robustness
12
Platform | Typical TDP | Peak TDP | Passive cooling | ECC / safety
TDA4VM | 5 W | 10 W | Excellent | L3 + DRAM / ASIL-D target
RK3588 | 8 W | 12 W | Good | No ECC
i.MX 95 | 5 W | 8 W | Excellent | DRAM ECC / safety support
i.MX 8M Plus | 3 W | 5 W | Excellent | DRAM ECC / IEC 61508
QCS6490 | 6 W | 9 W | Moderate | No ECC
Orin NX | 10 W | 25 W | Poor | No ECC
Sealed enclosure
Passive cooling is preferred for industrial deployments.
Reliability
ECC becomes important for safety-oriented designs.
Thermal risk
Orin NX may require active cooling or a large heatsink.
Technical Evaluation • Internal Use • Revision 1.0
13

## Slide 14
Software Ecosystem & Development
C/C++, Linux, RTOS and edge-AI integration
13
Platform | Linux BSP | RTOS | AI stack | Video / vision
TDA4VM | Yocto / Debian | FreeRTOS / SafeRTOS / QNX | TIDL, TFLite, ONNX | GStreamer, V4L2
RK3588 | Buildroot / Yocto / Debian | — | RKNN, TFLite, ONNX | MPP, GStreamer, V4L2
i.MX 95 | Yocto | FreeRTOS / Zephyr | eIQ, TFLite, ONNX | V4L2
i.MX 8M+ | Yocto / Android | FreeRTOS | eIQ, TFLite, ONNX | V4L2
QCS6490 | Qualcomm Linux / Android | — | QNN, SNPE | QMMF
Orin NX | JetPack / Ubuntu | — | TensorRT, TFLite, ONNX | V4L2 / GStreamer
Best deterministic architecture
TDA4VM: Linux AV pipeline + dedicated R5F RTOS control plane.
Best AI developer ecosystem
Orin NX: CUDA + TensorRT, subject to environmental constraints.
Technical Evaluation • Internal Use • Revision 1.0
14

## Slide 15
Recommendations by Application Profile
Match platform to the system-level mission
14
1
Safety-critical industrial vision + conferencing
TDA4VM / AM68A
Safety, deterministic control, harsh temperature
2
Multi-channel AI video gateway
RK3588
8K codec bandwidth + 6 TOPS NPU
3
Long-life industrial HMI
i.MX 95
2038+ supply + TSN + moderate AI
4
Cost-sensitive smart camera
i.MX 8M Plus
Low power + 1080p60 + proven industrial platform
5
High-performance non-critical robotics
QCS6490 / Orin NX
Extreme AI throughput; relaxed temperature requirement
Technical Evaluation • Internal Use • Revision 1.0
15

## Slide 16
Procurement & Supply-Chain Considerations
Lifecycle, availability and lead-time perspective
15
Vendor | Longevity | Industrial module availability | Lead-time risk
Texas Instruments | 2036+ | High | Low
Rockchip | 2033+ | High | Medium
NXP | 2036–2038+ | Very High | Low
Qualcomm | 2036+ | Medium | Medium
NVIDIA | 2033+ | High | Low–Medium
Certification priority
For IEC 61508 / ISO 26262 or 10+ year supply locks, the report prioritises NXP and TI.
Cost / performance
RK3588 offers strong performance-per-dollar but may need additional environmental qualification.
Procurement gate
Validate exact SoM, carrier, temperature grade and supplier lifecycle—not just SoC family.
Technical Evaluation • Internal Use • Revision 1.0
16

## Slide 17
Final Decision Matrix
System-level selection outcome
16
Rank | Platform | Primary strength | Key constraint | Decision
1 | TI TDA4VM / AM68A | Best overall industrial balance | Lower peak AI than Orin NX | RECOMMENDED
2 | Rockchip RK3588 | Best codec + cost efficiency | Safety ecosystem qualification | RECOMMENDED
3 | NXP i.MX 95 | Long-life + TSN | 2 TOPS AI | RECOMMENDED
4 | NXP i.MX 8M Plus | Low-power 1080p | Limited to 1080p-class AV | RECOMMENDED
5 | Qualcomm QCS6490 | 12 TOPS + 4K AV | −30°C minimum | CONDITIONAL
6 | NVIDIA Orin NX | 100 TOPS + CUDA/TensorRT | −25°C minimum, higher TDP | CONDITIONAL
Selection gate
If −40°C operation, deterministic RTOS control and industrial safety are mandatory, TDA4VM / AM68A is the report's primary decision.
Technical Evaluation • Internal Use • Revision 1.0
17

## Slide 18
Conclusion & Recommended Direction
01 PRIMARY
TI TDA4VM / AM68A Best balance of AI, AV, safety, deterministic control and industrial temperature.
02 SECONDARY
Rockchip RK3588 Preferred when 8K multimedia bandwidth and cost efficiency dominate.
03 CONDITIONAL
QCS6490 / Orin NX Use for extreme AI performance only when temperature constraints are relaxed.
Recommended next step: prototype the selected industrial SoM with the target camera, AI model, codec pipeline and thermal enclosure before design freeze.
Source basis: Industrial-Grade Edge AI Processor Selection Report • Rev 1.0 • 13 Aug 2026